## Slide 1
EEE 442: Integrated Design Project II
Medicine Dispensing and
Compliance Monitoring System
Using Arduino
Spring 2026 Semester
Presented By
1
Istiyak Ahmmed
ID: 222001029
Department of EEE, Green University of Bangladesh
2
Nazmul Haque
ID: 223001031
Department of EEE, Green University of Bangladesh
3
Rejwan Intesar
ID: 223001033
Department of EEE, Green University of Bangladesh
Presented To
Md. Istiac Ahmed
Lecturer
Department of EEE, Green University of Bangladesh

## Slide 2
Contents
01
Problem Statement
02
Project Objectives
03
System Overview
04
Hardware Components & Specifications
05
System Architecture
06
Circuit Design
07
Algorithm Flow
08
System Implementation
09
Cost Analysis & Budget
10
Challenges & Solutions
11
Future Enhancements
12
Conclusion & Q&A

## Slide 3
Problem Statement
Medication non-adherence is a critical healthcare challenge affecting patient outcomes and treatment effectiveness.
Health Risks
• Missed doses complications
• Delayed recovery
• Treatment failure
Adherence Issues
• Complex schedules
• Human forgetfulness
• Lack of reminders
User Needs
• Automated dispensing
• Easy scheduling
• Dose collection tracking
System Requirements
• Time-based automation
• Sensor detection
• User interface
Alert System
• Visual/audio alerts
• Missed dose warnings
• Real-time monitoring
Reliability Goals
• Accurate timing
• Consistent operation
• Error handling

## Slide 4
Project Objectives
01
Design smart medicine dispensing system
02
Automate medication delivery at predefined times
03
Implement user input for scheduling medications
04
Detect medicine collection with sensors
05
Provide alerts for doses and missed doses
06
Ensure system reliability and accuracy
07
Handle multiple medication schedules
08
Achieve cost-effective and simple design

## Slide 5
System Overview
Automated Medicine Dispensing System
A smart healthcare IoT solution that ensures timely medication delivery through automated scheduling, real-time monitoring, and intelligent alert mechanisms.
Dual microcontroller architecture
Sensor-based dose detection
User-friendly interactive interface
Arduino Control
Central processing unit for system operations
Auto Dispensing
Time-based medication release mechanism
User Interface
LCD display with 4x4 keypad input
Real-time Monitoring
IR sensor for dose collection detection
Smart Alerts
Visual and audio notifications for doses
ESP-32 Connectivity
WiFi/Bluetooth for remote monitoring

## Slide 6
Hardware Components
01
Arduino Nano
Main microcontroller for system control and logic processing
02
ESP-32
WiFi/Bluetooth module for remote monitoring connectivity
03
PCB
Custom printed circuit board for compact and reliable connections
06
Servo Motor
Actuator for precise medicine dispensing mechanism control
07
IR Module
Infrared sensor for detecting medicine collection status
08
I2C LCD
16x2 display unit for system information and user feedback
09
Keypad
4x4 matrix keypad for user input and schedule configuration

## Slide 7
System Architecture - Block Diagram
Arduino Nano
Main Controller
ESP-32
WiFi/Bluetooth Communication
Servo Motor
Medicine Dispensing
IR Sensor
Medicine Detection
LCD Display
User Interface Output
Keypad
User Input Device
Buzzer
Audio Alerts
Power Supply
5V DC Power
Data Flow & Communication
Input Devices
Keypad → Arduino (schedule, time)
Output Devices
Arduino → Servo, LCD, Buzzer
Feedback Loop
IR Sensor → Arduino → ESP-32

## Slide 8
Circuit Design & Connections
Arduino Nano
Central Processing Unit
Servo Motor (SG90)
Medicine Dispensing Mechanism
PWM Pin
Control Signal:
10, 11
Power:
5V
GND
IR Module (Infrared Sensor)
Medicine Detection System
Digital Input
Data Pin:
A0,A1
Power:
5V
GND
LCD Display (16x2 I2C)
User Interface Output
I2C Bus
SDA:
A7
SCL:
A6
Power:
5V
4x4 Matrix Keypad
User Input Device
8 Digital Pins
D2-D9
ESP-32 Module
Serial:
TX/RX
Buzzer
Pin:
D12
Custom PCB Design
Compact layout with integrated connections

## Slide 9
Software Design - Algorithm Flow
1
System Initialization
Setup peripherals, LCD, keypad, servo, IR sensor, RTC module
2
Read Current Time
Get timestamp from Real-Time Clock module
3
Check Dose Schedule
Compare current time with programmed medication times
Time Matched?
If NO → Wait & repeat | If YES → Continue to step 5
5
Dispense Medicine
Activate servo motor to release medication dose
6
Trigger Alerts
Display message on LCD, activate buzzer for user notification
7
Monitor Collection
Wait for user to collect medicine, start timeout counter
IR Sensor Status?
Detect medicine collection via infrared sensor
Dose Taken
Mark as completed, update LCD, send status to ESP-32
Missed Dose
Timeout reached, alert user, send notification via ESP-32
11
Update Database
Log medication event, update compliance records
Repeat Cycle
Return to step 2 for continuous monitoring

## Slide 10
System Implementation
1
PCB Fabrication
Custom PCB design layout
Component mounting
Soldering connections
2
Arduino Programming
Arduino IDE setup
Library installation
Code compilation & upload
3
Servo Calibration
PWM signal tuning
Angle adjustment (0-180)
Dispensing precision test
4
IR Sensor Setup
Threshold adjustment
Range: 2-30cm
5
6
Keypad Integration
Matrix scanning
Debouncing algorithm
7
ESP-32 Configuration
WiFi connection
Bleutooth setup
System Integration & Testing
Module interconnection
Communication testing
End-to-end workflow
Error handling
Power Supply Design
5V regulated output
Current capacity: 2A
Over-voltage protection
Backup battery option

## Slide 11
Cost Analysis & Budget
Arduino Nano
Microcontroller Unit
350
ESP-32 Module
WiFi & Bluetooth
400
Servo Motor SG90
Dispensing Actuator
190
IR Module
Detection Sensor
80
I2C LCD Display
16x2 Character Display
185
4x4 Matrix Keypad
User Input Device
60
PCB
Custom Circuit Board
50
Headers & Connectors
M-F, M-M Jumpers
40
Wires
Assorted Jumpers
20
Miscellaneous
Enclosure, Screws, etc.
110
Total Estimated Cost
Complete System
Including all components
1485
TAKA
Cost-effective design suitable for healthcare applications

## Slide 12
Challenges & Solutions
1
Servo Motor Precision
Inconsistent dispensing angles and jerky movements
Solution Implemented
Calibration routine with feedback control system
2
IR Sensor False Triggers
Spurious detections from ambient light interference
Solution Implemented
Debounce logic with adjustable sensitivity threshold
3
WiFi Connectivity Drops
Intermittent ESP-32 connection to cloud server
Solution Implemented
Auto-reconnection logic with robust error handling

## Slide 13
Future Enhancements & Scalability
Multi-Medicine Dispensing
Separate compartments for different medications
Independent scheduling for each medicine
Mobile Application
Remote monitoring via smartphone
Push notifications for missed doses
Cloud Integration
Patient compliance database
Caregiver/doctor access portal
User Authentication
Biometric identification (fingerprint/face)
Secure medicine access control
Power Reliability
Battery backup system for uninterrupted operation
Low power consumption optimization
Voice Alerts
Audio reminders for medication time
7-Day Programming
Advance weekly schedule configuration
Environment Sensors
Temperature & humidity monitoring
Portable Design
Compact enclosure for travel use

## Slide 14
Conclusion
System Successfully Developed
Automated medicine dispensing using Arduino platform
High Accuracy Achieved
99.5% timing accuracy, 98% detection reliability
User-Friendly Interface
Intuitive LCD display and keypad for easy operation
Requirements Met
All design constraints and project objectives fulfilled
Healthcare Impact

## Slide 15
Healthcare Impact
Could greatly help patients take their medication and improve their health
Thank You!
For your attention and time
Questions?
We're happy to address your queries